Kalman filters

Linear Kalman Filter

Optimal estimate for linear dynamical systems.
Recursive estimation from noisy measurements.

,
x – states to be estimated
u – input signal, if any
z – measurements
w – process noise
z – measurement noise
In the algorithm, the covariance matrices of w and v is also required.

From triangulation we get the location x = f(%theta_1, %theta_2) , where f is a nonlinear function since it contains several sine/cosine functions with %theta_1 and %theta_2 as arguments.
Standard Kalman filter can not be applied.

Extended Kalman filter

The model need not be linear, instead:

where f and h can be any differentiable non-linear functions.
The Extended Kalman filter linearises the model around the best state estimate and apply the Kalman filter to the resulting system.
This requires the Jacobian of the functions f and h and thus their partial derivatives.

Iterated Extended Kalman Filter
Relinearize the model after a measurement update with a (hopefully) improved estimate and apply the Extended Kalman filter.

Unscented Kalman filter

The required mean and covariance matrices are parametrized using carefully chosen weighted samples.
The system is applied to each sample, which means that we get the propagated mean and covariance of the system.
No linearization involved in the propagation of the mean and covariance, so no Jacobians are needed.
More accurate than the Extended Kalman Filter, especially for highly non-linear systems.